## Slide 1: Moving and Maneuvering

## Slide 2: Two types of drag
Viscous Drag
  Skin Friction Drag
  Negligible for ROV
Pressure drag
  Cause by the mass of fluid
  Dominates in big objects
  Creates high and low pressure zones that causes turbulence

## Slide 3: Theoretical Approach
D = Drag (in Newtons)
P = Fluid Density (kilograms per cubic meters)
  1,000 kg/m^3 for water
Cd = Drag Coefficient
  1 for ROV
A = Frontal Area (Square meters)
  Estimate by finding frontal area of smallest box the ROV can fit into
U = Speed through Fluid (meters per second)

## Slide 4: Empirical Approach

## Slide 5: Types of motor
Brushed DC motors
  Least Expensive
  Most common on ROVs
Brushless motors
  More reliable
  More expensive
Stepper motors and Servo Motors
  Precision control
Gear Motors
  Gears attached to shaft to increase torque

## Slide 6: Brushed vs Brushless Motors
 | Brushed (BDC) | Brushless (BLDC)
External Motor Controller | Optional | Required
Price | Less Expensive | More expensive
Efficiency | 75 – 80% | 85 – 90%
Sparkles Commutator | No | Yes
Heat Dissipation | No | Yes
Reliability | Good | Excellent

## Slide 7: Gears
Increase Torque at Lower Speeds
Gear Ratio
  Signify the increase in Torque
Planetary Gears
  Planets orbiting a star
  Beneficial for thrusters and claws
  Recommend ratio: 4 to 8

## Slide 8: Propellers
Most common device used in ROV
Creates a strong pressure difference that accelerate water backwards
  Third law pushes ROV forward
Standard
Kort Nozzles
  Have a special shaped housing unit around the propellers
Hubless propellers
  Have no center shaft

## Slide 9: Properties to pay attention to
Diameter
Pitch: Distance the angle of the blades would move the propeller forward after one full rotation
Number of blades
  Lower blades are more efficient
  More blades can push or pull harder at lower speeds
Blade Shape:
  Long, Skinny blades are more efficient under light loads, but can achieve high force
  Short, wide blades are less efficient but can achieve higher forces
Method of Attaching Prop Hub to Shaft: Easily attachable and should fit snugly

## Slide 10: Thruster Arrangement

## Slide 11: Benefits and Drawbacks
H - Drive |  | X - Drive | 
Benefits | Drawbacks | Benefits | Drawbacks